NSRDB Data Dictionary (Solar Fields)

March 20, 2007

| Field | Description | Units | Resolution |
| --- | --- | --- | --- |
| 1 | Date | YYYY-MM-DD |  |
| 2 | Time (LST) | HH:MM |  |
| 3 | Hourly mean zenith angle (for sunup periods) | Decimal degrees | 0.1˚ |
| 4 | Hourly mean azimuth angle (for sunup periods) | Decimal degrees | 0.1˚ |
| 5 | Hourly extraterrestrial radiation on a horizontal surface | W/m2 | 1Watt |
| 6 | Hourly extraterrestrial radiation normal to the sun | W/m2 | 1Watt |
| 7 | Modeled Global Horizontal | W/m2 | 1Watt |
| 8 | Modeled Global Horizontal Source Flag (Note 1) |  |  |
| 9 | Modeled Global Horizontal Uncertainty | ± % | 1% |
| 10 | Modeled Direct Normal | W/m2 | 1Watt |
| 11 | Modeled Direct Normal Source Flag (Note 1) |  |  |
| 12 | Modeled Direct Normal Uncertainty | ± % | 1% |
| 13 | Modeled Diffuse Horizontal | W/m2 | 1Watt |
| 14 | Modeled Diffuse Horizontal Source Flag (Note 1) |  |  |
| 15 | Modeled Diffuse Horizontal Uncertainty | ± % | 1% |
| 16 | Measured Global Horizontal | W/m2 | 1Watt |
| 17 | Measured Global Horizontal Quality Flag (Note 2) | SERI QC |  |
| 18 | Measured Direct Normal | W/m2 | 1Watt |
| 19 | Measured Direct Normal Quality Flag (Note 2) | SERI QC |  |
| 20 | Measured Diffuse Horizontal | W/m2 | 1Watt |
| 21 | Measured Diffuse Horizontal Quality Flag (Note 2) | SERI QC |  |
| 22 | *Precipitable water | Centimeters | 1 cm |
| 23 | *Precipitable water Flag (Note 4) |  |  |
| 24 | *Aerosol optical depth, Broadband | [Unitless] | 0.001 |
| 25 | *Aerosol Optical Depth Flag (Note 5) |  |  |

*Asterisks indicate a field is subject to data filling. Completeness of these fields is used to determine if a site has a “complete period of record.” Other fields may have gaps even if these fields are complete.

Notes

Note 1:  Solar Field Source Flag values:

| Flag | Description |
| --- | --- |
| 1 | Value modeled from METSTAT |
| 3 | Value time shifted from SUNY Satellite model |
| 4 | Value time shifted from SUNY satellite model, adjusted to a minimum low-diffuse envelope |
| 99 | Data are missing (associated data field is filled with -9900) |

Note 2: NREL SERI QC Flag convention

| Flag | Description |
| --- | --- |
| 00 | Untested (raw data) |
| 01 | Passed one-component test; data fall within min-max limits of Kt, Kn, or Kd |
| 02 | Passed two-component test; data fall within 0.03 of the Gompertz boundaries |
| 03 | Passed three-component test; data come within ± 0.03 of satisfying Kt=Kn+Kd |
| 04 | Passed visual inspection; not used by SERI_QC |
| 05 | Failed visual inspection; not used by SERI_QC |
| 06 | Value estimated; passes all pertinent SERI_QC test |
| 07 | Failed one-component test; lower than allowed minimum |
| 08 | Failed one-component test; higher than allowed maximum |
| 09 | Passed three-component test but failed two-component test by > 0.05 |
| 10-93 | Failed two- or three-component tests in one of four ways. To determine the test failed and the manner of failure (high or low), examine the remainder of the calculation (flag + 2)/4. REM Failure 0 Parameter too low by three-component test (Kt=Kn+Kd) 1 Parameter too high by three-component test (Kt=Kn+Kd) 2 Parameter too low by two-component test (Gompertz boundaries) 3 Parameter too high by two-component test (Gompertz boundaries) The magnitude of the test failure (distance in K-units) is determined from: d = (INT (flag +2)/4)/100. |
| 94-97 | Data fall into a physically impossible region where Kn > Kt by K-space distances of 0.05 to 0.10 (94), 0.10 to 0.15 (95), 0.15 to 0.20 (96) amd ± 0.20 (97). |
| 98 | Not used |
| 99 | Missing data (associated data field is filled with -9900) |

Note 3: Meteorological Data Flag values:

| Flag | Description |
| --- | --- |
| 0-9 | ISH data flags (unmodified data) |
| 51 | Value from short-term data filling or interpolation |
| 52 | Value from medium-term data filling |
| 53 | Value from long-term data filling |
| 54 | Value is calculated: relative humidity calculated from dry bulb and dew point temperatures station pressure calculated from sea level pressure, altimeter, and dry bulb or data point undefined by convention (wind direction at zero speed) |
| 55 | Value from last-ditch data filling |
| 56 | Value statistically derived (cloud amounts based on probability tables) |
| 61 | Value is modeled (total and opaque cloud derived from Supplemental Cloud Product; ceiling height as linear function of opaque cloud amount) |
| 99 | Value is missing (associated data field is filled with -9900) |

Note 4: Precipitable Water Flag values

| Flag | Description |
| --- | --- |
| 1 | From NVAP 1x daily from 1˚ x 1˚ grid |
| 2 | NVAP 2x daily from 0.5˚ x 0.5˚ grid |
| 3 | From NARR 8x daily from 32 km grid |
| 4 | From 2x daily radiosonde |
| 51-55 | (see note 3) |

Note 5: AOD Flag values

| Flag | Description |
| --- | --- |
| 1 | DNI inverted measurements for CSR model (ca 1995) |
| 2 | From Southwest US study by George and Gueymard, ca. 2001 using sun photometry and spectral data |
| 3 | From MISR, George and Gueymard, ca. 2004. |
| 51-55 | (see note 3) |

The AOD field will contain either monthly mean smoothed or monthly mean randomized values, depending on the solar model source flag:

| Model Source Flag | Randomized | Smoothed |
| --- | --- | --- |
| 1 | X |  |
| 2, 3, 99 |  | X |

Randomized AOD is the value used by the MESTAT model. This is the log-normal randomized value based on the daily mean-preserving smoothed data derived from monthly means. All AOD values include a Mt. Pinatubo eruption modifier for 2001-2004.